## Slide 1: EE 421 / CS 425 Digital System Design Laboratory 1
Fall 2024
Shahid Masud

## Slide 2: Lab Course Learning Objectives
Describe, Simulate and Debug combinational and sequential digital systems using SystemVerilog hardware description language (Design Capture).
Understand Design Flow and EDA tools for Simulation and Synthesis of FPGA design of digital systems.
Implement and test digital systems on FPGA platforms (hardware boards).

## Slide 3: Course Outline and Grading Scheme
Lab Completion (10 to 11 Labs): 50%
  Lab Attendance (1% each lab)
  TA grades the Task Completion (2% each lab)
  Submitting Reports and Observations, as required (2% each lab)
Lab Projects (1 to 2): 30%
  SystemVerilog coding and Testbench
  Simulation
  Synthesis
  FPGA prototyping
  Project report
  Presentation
Lab (Midterm) Exam: 20%
MS Grading: Final Grade is Combined (80% Theory, 20% Lab)

## Slide 4: Today’s Topics
Learning Objectives
Lab Course Outline and Grading
RTL Design - Introduction
Design Flow – from idea to product
Step through EDA tools
Introduction to SystemVerilog and Design Methodology
Tools Installation

## Slide 5: RTL View of Digital System Design
RTL = Register Transfer Logic
Input
Register
Output
Register
Trigger
Trigger
Combinational Logic Cloud
A Complex Digital System has many RTL Modules
External
Input
External
Output
Engineering System has Inputs and Outputs
This is One RTL Module

## Slide 6: RTL Design with a Pipeline Cut
RTL = Register Transfer Logic
Input
Register
Output
Register
Trigger 1
Trigger 2
Combinational Logic Cloud
External
Input
External
Output
Pipeline
Cut
Pipelined RTL
Input
Register
Output
Register
Trigger 1
Trigger 3
Combinational Logic
External
Input
External
Output
Pipeline Cut
Combinational Logic
Pipeline
Register
Trigger 2
What is achieved?

## Slide 7: Design Flow – from idea to product
Customer
(Mobile Phone Company)
Sales Team and Senior Managers
Engineering Staff
Chip / FPGA Manufactured
Engineering EDA Steps (next slide)
Product
Description
High-Level Specifications
Testing and Verification
Modular Specifications

## Slide 8: Step Through EDA Tools
Design Capture
Functional Simulation
Synthesis
Post-Synthesis Simulation
Place and Route
Product FPGA / ASIC
Timing, Power, Area
Text Editor
Questa
Xilinx Vivado
Questa
Xilinx Vivado

## Slide 9: Simulation Tool Questa

## Slide 10: Synthesis Tool Xilinx Vivado

## Slide 11: Place and Route – Xilinx (FPGA) Technology

## Slide 12: Post Layout Design on Xilinx FPGA

## Slide 13: Hardware Description Languages - SystemVerilog
Specialized Computer Language for Capturing Hardware Design Idea
Can be used to describe structure and behavior of digital circuits
HDL include notion of hardware specific time or delay
They have support for Concurrency which is peculiar to hardware
Remember 3 distinct features of HDL not available in other
Programming languages

## Slide 14: SystemVerilog
Verilog is a Hardware Description Language that was Standardized by IEEE through Standard IEEE-1364-2001, first proposed in 1995
Most Verilog constructs can be Simulated and Synthesized
System Verilog includes some extensions for high-level object-oriented design and first became IEEE standard in 2008
VHDL is another HDL (Very High-Speed Integrated Circuit HDL), 1987
VHDL is strictly typed language and allows complex data types
Both Verilog and VHDL are used worldwide
SystemVerilog is becoming popular as it incorporates UVM features for verification; latest IEEE Standard 1800-2023, previous 2017, 2012

## Slide 15: Design Capture in SystemVerilog HDL
SystemVerilog Allows Design Capture at Various Hierarchy Levels:
Switch Level (NMOS and PMOS transistors)
Gate Level (Describing Circuit as Logic Gates)
  Basic Functions of Gates are available as Primitives
Data Flow (RTL) Level Design
Behaviour Level Design
The Design is captured in a text file or it can be obtained from
schematic diagram
CMOS VLSI
Design
Structural
Design like
Schematic

## Slide 16: SystemVerilog Syntax

## Slide 17: Structural SystemVerilog (port mapping)
Components available in library are port mapped
Also an example of Hierarchical Design

## Slide 18: Behavioral SystemVerilog (assign statement)
This is the Highest Level of Abstraction in HDL
Different Circuit blocks can be represented as Functions, Tasks and Hierarchical Modules
‘Assign’ and ‘Always’ are relevant constructs

## Slide 19: RTL in SystemVerilog (always blocks)
RTL =Register Transfer Level
Module is described in Verilog in the form of Data Flow
Signals are assigned by the data operation
Design is Implemented using Concurrent Assignments
‘Always’ and ‘Clk’ are relevant constructs

## Slide 20: Modular Approach in SystemVerilog
Module is a basic building block in SystemVerilog
Module can be a collection of multiple low level logic blocks
Modules are interconnected through Port Interface
Internal functionality of any Module can be altered without affecting any other Module

## Slide 21: Use of Parameter and Generate in SystemVerilog

## Slide 22: Hierarchical Approach in SystemVerilog
Instantiation allows creation of Hierarchy in SystemVerilog.
The Modules that are used in another Module are called Instances or Instantiation.
Nesting of Modules is not permitted as it is Hardware Design.
One Module can be used in many other Modules through Instantiation
4 to 1 MUX using 2 to 1 MUX
Design Reuse

## Slide 23: Design Abstraction in SystemVerilog
Two Design Methodologies
Top-Down Methodology
  We define the top-level block and identify the Sub Blocks
needed to build the top-level block
  These Sub Blocks are further divided until we come to Leaf
Cells which cannot be further Sub Divided
Bottom-Up Methodology
  We first Identify the Building Blocks (Leaf Cells) that are
available to us in a library
  We build bigger blocks using these Building Blocks
  The process continues until we reach the Top-Level block

## Slide 24: Test Bench in HDL
Used for Functional as well as Post-Synthesis Testing
Timing Information can be added through Gate Models
Stimulus through Test Bench or External File
Design Under Test DUT
Monitor
Timing Diagrams, File Comparison

## Slide 25: Writing Test Benches in SystemVerilog
Wrapper SV Module
SV Module
Input Ports
Output Ports
Stimulus
Signals
Screen Display
Or File Write
Clock
Instantiation
SV = SystemVerilog file extension

## Slide 26: RTL Synthesis

## Slide 27: Lab 1 Task – EDA Tools Installation
Refer to Lab Manual 1 and Appendix A
--------------- for own learning ---------------------
SystemVerilog language https://www.chipverify.com/tutorials/systemverilog
Online EDA tools (iverilog) for simulation and testing
https://courses.edaplayground.com/home