## Slide 1: Lecture 3 EE 421 / CS 425 Digital System Design
Fall 2024
Shahid Masud

## Slide 2: Topics
Quine McCluskey method of Logic Minimization
Boolean Simplification using n-cube
WinLogiLab Software Demo
Examples using WinLogiLab Software Tool

## Slide 3: Problem with Logic Minimization
Boolean Algebra and K-Maps can easily solve 4 variables.
Beyond 5 or 6 input variables, we have to look for some other scalable techniques.
The techniques should be systematic and programmable

## Slide 4: Quine McCluskey Method – Example 1
Make Table of Minterms
Count No of 1s
Minterms | Binary | No of 1s
2 | 0010 | 1
4 | 0100 | 1
6 | 0110 | 2
8 | 1000 | 1
9 | 1001 | 2
10 | 1010 | 2
12 | 1100 | 2
13 | 1101 | 3
15 | 1111 | 4

## Slide 5: Quine McCluskey – Example 1 - contd
Table of Minterms
Group as per number of 1s
Minterms | Binary | No of 1s
2 | 0010 | 1
4 | 0100 | 1
8 | 1000 | 1
6 | 0110 | 2
9 | 1001 | 2
10 | 1010 | 2
12 | 1100 | 2
13 | 1101 | 3
15 | 1111 | 4
Group of one 1s
Group of two 1s
Group of three 1s
Group of four 1s
List 1

## Slide 6: Quine McCluskey – Example 1 - contd
Check each entry with an entry in higher block.
See if there is any entry with One bit change only. These entries can be combined.
If any entry cannot be combined, it is a Prime Implicant.
Mark a tick  where combined.
In Combined terms, put a ‘–’ where both 1 and 0 exist in the two terms
Minterm | Binary | Combined or PI
2, 6 | 0-10 | 
2, 10 | -010 | 
4, 6 | 01-0 | 
4, 12 | -100 | 
8, 9 | 100- | 
8, 10 | 10-0 | 
8, 12 | 1-00 | 
9, 13 | 1-01 | 
12, 13 | 110- | 
13, 15 | 11-1 | 
List 2
Minterm | Binary | Combine or PI
2 | 0010 | 
4 | 0100 | 
8 | 1000 | 
6 | 0110 | 
9 | 1001 | 
10 | 1010 | 
12 | 1100 | 
13 | 1101 | 
15 | 1111 | 
List 1










## Slide 7: Quine McCluskey – Example 1 - contd
Minterm | Binary | Combined or PI
2, 6 | 0-10 | 
2, 10 | -010 | 
4, 6 | 01-0 | 
4, 12 | -100 | 
8, 9 | 100- | 
8, 10 | 10-0 | 
8, 12 | 1-00 | 
9, 13 | 1-01 | 
12, 13 | 110- | 
13, 15 | 11-1 | 
List 2
Minterm | Binary | Combine or PI
2 | 0010 | 
4 | 0100 | 
8 | 1000 | 
6 | 0110 | 
9 | 1001 | 
10 | 1010 | 
12 | 1100 | 
13 | 1101 | 
15 | 1111 | 
List 1
Minterm | Binary | Combined or PI
(8, 9), (12, 13) | 1-0- | 
(8, 12), (9, 13) | 1-0- | 
List 3




PI1
Same PI1
PI2
PI3
PI4
PI5
PI6
PI7

## Slide 8: Quine McCluskey – Example 1 - contd
Minterm | Binary | Combined or PI
2, 6 | 0-10 | 
2, 10 | -010 | 
4, 6 | 01-0 | 
4, 12 | -100 | 
8, 9 | 100- | 
8, 10 | 10-0 | 
8, 12 | 1-00 | 
9, 13 | 1-01 | 
12, 13 | 110- | 
13, 15 | 11-1 | 
List 2
Minterm | Binary | Combine or PI
2 | 0010 | 
4 | 0100 | 
8 | 1000 | 
6 | 0110 | 
9 | 1001 | 
10 | 1010 | 
12 | 1100 | 
13 | 1101 | 
15 | 1111 | 
List 1
Minterm | Binary | Combined or PI
(8, 9), (12, 13) | 1-0- | 
(8, 12), (9, 13) | 1-0- | 
List 3




PI1
Same PI1
PI2
PI3
PI4
PI5
PI6
PI7

## Slide 9: Quine McCluskey Method - contd
To find minimum number of Prime Implicants, make a PI Chart. PI vs Minterms covered
PI Needed | Minterm to cover | 2 | 4 | 6 | 8 | 9 | 10 | 12 | 13 | 15
 | PI1 |  |  |  | X | X → Ⓧ |  | X | X | 
Eliminate | PI2 | X |  | X |  |  |  |  |  | 
 | PI3 | X |  |  |  |  | X |  |  | 
 | PI4 |  | X | X |  |  |  |  |  | 
Eliminate | PI5 |  | X |  |  |  |  | X |  | 
Eliminate | PI6 |  |  |  | X |  | X |  |  | 
 | PI7 |  |  |  |  |  |  |  | X | X → Ⓧ
This symbol Ⓧ means this PI is the only cover for this particular Minterm









PI1=1-0-, PI2=0-10, PI3=-010
PI4=01-0, PI5=-100, PI6=10-0
PI7=11-1

## Slide 10: Quine McCluskey Method - contd
To find minimum number of Prime Implicants, make a PI Chart. PI vs Minterms covered
PI Needed | Minterm to cover | 2 | 4 | 6 | 8 | 9 | 10 | 12 | 13 | 15
 | PI1 |  |  |  | X | X → Ⓧ |  | X | X | 
Eliminate | PI2 | X |  | X |  |  |  |  |  | 
 | PI3 | X |  |  |  |  | X |  |  | 
 | PI4 |  | X | X |  |  |  |  |  | 
Eliminate | PI5 |  | X |  |  |  |  | X |  | 
Eliminate | PI6 |  |  |  | X |  | X |  |  | 
 | PI7 |  |  |  |  |  |  |  | X | X → Ⓧ
This symbol Ⓧ means this PI is the only cover for this particular Minterm









PI1=1-0-, PI2=0-10, PI3=-010
PI4=01-0, PI5=-100, PI6=10-0
PI7=11-1

## Slide 11: Quine McCluskey Method - contd
= PI1 + PI3 + PI4 + PI7
= 1-0- + -010 + 01-0 + 11-1
= AC’ + B’CD’ + A’BD’ + ABD
Minterm | Binary | Combine or PI
2, 6 | 0-10 | PI2
2, 10 | -010 | PI3
4, 6 | 01-0 | PI4
4, 12 | -100 | PI5
8, 9 | 100- | 
8, 10 | 10-0 | PI6
8, 12 | 1-00 | 
9, 13 | 1-01 | 
12, 13 | 110- | 
13, 15 | 11-1 | PI7
Minterm | Binary | Combineor PI
(8, 9), (12, 13) | 1-0- | PI1
(8, 12), (9, 13) | 1-0- | Same PI1

## Slide 12: Quine McCluskey – Example 1 - contd
Answer:
f(A,B,C,D) = PI1 + PI3 + PI4 + PI7
= 1-0- + -010 + 01-0 + 11-1
=

## Slide 13: QM with Don’t Care and 5 Variables
+ d (5, 18, 19, 21, 23) these are don’t care terms
List all minterms, note number of 1’s
Include don’t care terms in logic simplification
Minterms | Binary | No of 1s
2 | 00010 | 1
3 | 00011 | 2
7 | 00111 | 3
10 | 01010 | 2
12 | 01100 | 2
15 | 01111 | 4
27 | 11011 | 5
5 | 00101 | 2
18 | 10010 | 2
19 | 10011 | 3
21 | 10101 | 3
23 | 10111 | 4
Don’t Care Terms

## Slide 14: QM with Don’t Care and 5 Variables - contd
+ d (5, 18, 19, 21, 23) these are don’t care terms
Group minterms as per number of 1s
Include don’t care terms in logic simplification
Minterms | Binary | No of 1s
2 | 00010 | 1
3 | 00011 | 2
5 | 00101 | 2
10 | 01010 | 2
12 | 01100 | 2
18 | 10010 | 2
7 | 00111 | 3
19 | 10011 | 3
21 | 10101 | 3
15 | 01111 | 4
23 | 10111 | 4
27 | 11011 | 4

## Slide 15: QM with Don’t Care and 5 Variables - contd
+ d (5, 18, 19, 21, 23)
these are don’t care terms
List 1 – Combine with next higher block
Minterms | Binary | Combine or PI
2 | 00010 | 
3 | 00011 | 
5 | 00101 | 
10 | 01010 | 
12 | 01100 | make PI
18 | 10010 | 
7 | 00111 | 
19 | 10011 | 
21 | 10101 | 
15 | 01111 | 
23 | 10111 | 
27 | 11011 | 
Minterms | Binary | Combine or PI
2, 3 | 0001- | 
2, 10 | 0-010 | 
2, 18 | -0010 | 
3, 7 | 00-11 | 
3, 19 | -0011 | 
5, 7 | 001-1 | 
5, 21 | -0101 | 
18, 19 | 1001- | 
7, 15 | 0-111 | 
7, 23 | -0111 | 
19, 23 | 10-11 | 
19, 27 | 1-011 | 
21, 23 | 101-1 | 
List 2

## Slide 16: QM with Don’t Care and 5 Variables - contd
List 1 – Combine with next higher block
Minterms | Binary | Combine or PI
2 | 00010 | 
3 | 00011 | 
5 | 00101 | 
10 | 01010 | 
12 | 01100 | Make PI7
18 | 10010 | 
7 | 00111 | 
19 | 10011 | 
21 | 10101 | 
15 | 01111 | 
23 | 10111 | 
27 | 11011 | 
Minterms | Binary | Combine or PI
2, 3 | 0001- | 
2, 10 | 0-010 | Make PI4
2, 18 | -0010 | 
3, 7 | 00-11 | 
3, 19 | -0011 | 
5, 7 | 001-1 | 
5, 21 | -0101 | 
18, 19 | 1001- | 
7, 15 | 0-111 | PI5
7, 23 | -0111 | 
19, 23 | 10-11 | 
19, 27 | 1-011 | PI6
21, 23 | 101-1 | 
List 2 – Combine next higher block
Minterms | Binary | Combine or PI
(2, 3) , (18, 19) | -001- | PI1
(3, 7), (19, 23) | -0-11 | PI2
(5, 7), (21, 23) | -01-1 | PI3
List 3

## Slide 17: QM with 5 Variable, don’t care - contd
To find minimum number of Prime Implicants, make a PI Chart. PI vs Minterms covered
 |  |  |  |  |  |  |  | 
PI Needed | Minterm | 2 | 3 | 7 | 10 | 12 | 15 | 27
 | PI1 | X | X |  |  |  |  | 
Eliminate | PI2 |  | X | X |  |  |  | 
Eliminate | PI3 |  |  | X |  |  |  | 
 | PI4 | X |  |  | X →Ⓧ |  |  | 
 | PI5 |  |  | X |  |  | X →Ⓧ | 
 | PI6 |  |  |  |  |  |  | X →Ⓧ
 | PI7 |  |  |  |  | X →Ⓧ |  | 
This symbol Ⓧ means this PI is the only cover for this particular Minterm
PI1 = -001-
PI2 = -0-11
PI3 = -01-1
PI4 = 0-010
PI5 = 0-111
PI6 = 1-011
PI7 = 01100

## Slide 18: QM with Don’t Care and 5 Variables
+ d (5, 18, 19, 21, 23) these are don’t care terms
Answer f = PI1 + PI4 + PI5 + PI6 + PI7
= -001- + 0-010 + 0-111 + 1-011 + 01100
=

## Slide 19: Boolean Expression on n-cube
b
a
c
1
c
0
0 a 1
0 b 1
000
100
001
111
010
110
101
011
b
Vertex
Edge

## Slide 20: Minimization using Boolean n-cube
Repeatedly Combine Cubes that differ in only one literal
Eliminate Redundant Implicants
Grouping along multiple dimensions is possible

## Slide 21: Example 1 using n-cube
F=abc + abc’
= 111 + 110
abc = 000
100
110
111
011
101
001
010
c is changing in this
vertex so c can be
eliminated
Answer:
F = ab
Each Edge of Graph is
a minterm
Connection through Vertex
Shows some Adjacent term can be
eliminated
On-Set
Off-Set

## Slide 22: Example 2 using n-cube
F=abc + a’bc + abc’ + a’b’c + ab’c’ + a’b’c’
= 111 + 011 + 110 + 001 + 100 + 000
000
100
110
111
011
101
001
010
a
c
b

## Slide 23: First solution - Example 2 using n-cube
F=abc + a’bc + abc’ + a’b’c + ab’c’ + a’b’c’
= 111 + 011 + 110 + 001 + 100 + 000
000
100
110
111
011
101
001
010
Ignore Redundant Cover of
ab and a’b’
Answer:
F= a’c + bc + b’c’ + ac’
Combine Adjacent Vertex into one implicant

## Slide 24: Second solution - Example 2 using n-cube
F=abc + a’bc + abc’ + a’b’c + ab’c’ + a’b’c’
= 111 + 011 + 110 + 001 + 100 + 000
000
100
110
111
011
101
001
010
Ignore Redundant Cover of
a’c and ac
Answer:
F= a’b’ + b’c’ + bc + ab

## Slide 25: A Boolean n-Cube Graph for 4-variables
Ref: Youtube channel
‘Wrath of Math’
Add ‘0’ at MSB of
3-Cube graph
Extend all Edges of
3-Cube by adding
‘1’ at MSB to make
4-cube graph

## Slide 26: Graphs for 1 to 4 variables

## Slide 27: Example Graph for 4 variables

## Slide 28: Little bit about Espresso tool
Uses Graph Theory to represent Boolean variables
Finds different groupings to determine local and global minima
Keeps trying for optimal solution until some defined time-limit is reached
PyEDA library has logic minimization and synthesis tools in Python
https://pyeda.readthedocs.io/en/latest/overview.html
https://pyeda.readthedocs.io/en/latest/2llm.html

## Slide 29: Espresso - 1

## Slide 30: Espresso - 2

## Slide 31: Espresso - 3

## Slide 32: Espresso - 4

## Slide 33: Learn More on Espresso
DVD - Lecture 4a: Logic Synthesis - Part 2 (youtube.com)
https://www.youtube.com/watch?v=yJ5CaAk7Nq8&list=WL&index=1
Lec 13: ESPRESSO-Heuristic Based Switching Function Minimization (youtube.com)
https://www.youtube.com/watch?v=NRAoJ8eKIgM